## Slide 1: Yaw Angle Drift
6 November 2014
Patrick Healy
GN&C
iRobot
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1

## Slide 2: Observed Yaw Angle Drift
The Create robot was commanded to perform various laps around a square defined by 4 waypoints
  One set of data has the origin centered in the square
  Second data set has the origin offset on an outside corner
After completing the specified laps, the robot was commanded to the origin and to correct its attitude to due north (zero degrees in yaw angle)
When the origin command is complete, the yaw measurement will have drifted over time and there will be error between where the robot thinks the yaw angle is 0 degrees and true north
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1

## Slide 3: Recorded Data
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
Centered Origin
Offset Origin
Robot thinks it has returned to origin

## Slide 4: Recorded Data Zoomed in to Origin
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
Centered Origin
Offset Origin
Actual position
Actual position
Yaw angle drift is about the same for both cases
  Position drift is due to the yaw angle drift, which is why the position drift is much larger for the offset origin

## Slide 5: Possible Solutions for Yaw Drift
1) Spend more time working with the magnetometer drift correction
  This is currently turned off because it did not seem to produce usable rotation information
  Physical rotations did not match the output of the IMU when using the magnetometers
  Positive rotations and negative rotations of the same physical magnitude were not equivalent in the IMU output
2) Have a “north star” light on an arena wall
  This would require a 360 deg scan using the robot camera at some set interval to find true north
  Walls in the arena may eliminate this possibility
3) GPS to correct position
  No GPS available indoors
  Possibly would help correct position, and would help in commanding vehicles to new positions, but would not help with correcting the yaw orientation angle (if that type of control is needed)
4) Install color grid on floor and new color sensor on robot
  Possibly would help correct position (like in the case of GPS), and would help in commanding vehicles to new positions, but would not help with correcting the yaw orientation angle (if that type of control is needed)
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
Working on 1) and 4) seem like the most reasonable/productive

## Slide 6: Color Grid Options
7x7 m grid has 64 points to be defined in the color grid (if defining at every meter)
  Would require 8 led color combinations
  Even at 1 meter increments, there is still the chance that the robot would not cross over one of the 8LED markers with its sensor
Getting the position updates will help with commanding the vehicles to a new position, but it will not correct the yaw angle drift
  Commands to a new position are based on a change in the vehicle’s heading
  If a team needs to correct a vehicles orientation while the vehicle is stopped, the yaw angle drift will still be a factor
    It is possible that the teams will be commanding delta orientation changes and the drift will not be an issue
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
NORTHROP GRUMMAN PRIVATE/PROPRIETARY LEVEL 1
Arena Grid: 7x7 m